The Spaghetti Bridge

# Goal

- Make a bridge out of spaghetti that holds as much weight as possible.

# Materials

- You may only use spaghetti (no tubular or flat pastas) and glue (any kind of glue is fine)

- The maximum allowable mass is 2000 g

# Dimensions

- Your bridge must span a 100 cm gap between two tables of the same height.

- Maximum bridge height is 50 cm above the table height.

- Maximum bridge depth is 10 cm below the table height.

- Maximum bridge length is 110 cm.

- Maximum bridge width is 10 cm.

- Every bridge must have a solid deck (for cars, of course!) that passes between the two tables:

The deck may not rise or fall more than 5 cm.  
No gaps or spaces larger than 0.5 cm are allowed in any part of the deck.

A test car (6 cm x 6 cm x 10 cm) must fit and pass freely across your entire bridge deck.

# Bridge Design Resources

To test your design ideas before you start making your bridge, try out the great engineering program West Point Bridge Designer—it’s free!   http://bridgecontest.usma.edu/

- Every bridge must have a U-bolt or hanging point installed in the centre (see diagram below).  Weights will be hung from this point during testing.  The “platform” is the same size as the bottom of the test car (6 cm x 10 cm) and is designed to stop the U-bolt from tearing through your bridge deck when weight is added.

- You may make a copy and and install your own platform, or come to the competition with two holes  drilled in the centre of your bridge, each 0.7 cm wide, and 3.7 cm apart, as shown below:

# Testing

- The mass of your bridge will be recorded.

- The dimensions of your bridge will be checked.

- The deck will be inspected for gaps and the test car must pass freely across the entire deck.

- Weights will be hung from the centre of your bridge as follows:

1) one team member will add mass (minimum 100 g)

2) a judge will determine if the bridge is still stable

3) if the mass is held, it “counts” towards your score—you may go on

4) mass is added until your bridge is destroyed!

# Scoring

Mass held by bridge 	(more is better)

Mass of bridge 	(lighter is better)

Example:  	A 1250 g bridge that holds 3200 g has a score of    3200 ( 1250  =  2.56

A 650 g bridge that holds 1800 g has a score of      1800 ( 750    =  2.77

Record:  A David Thompson Secondary team scored 8.7 in JPEC 2005!

# Text boxes

test car

platform

deck