Spaghetti Water Tower

Goal:  	Build a tower that holds the largest volume 
of water but uses a minimum of spaghetti.

Design Rules:

Basic Dimensions

- The base of the tower must fit within a 
25cm x 25cm square, on a flat, level surface.

- The lowest point of the water container must 
be a minimum of 100cm above the ground.

Materials

- Spaghetti and glue are the only allow building materials for the tower

- The water container may be made of anything you wish but it's only purpose should be to hold water, not to help the tower stay upright.

Competition Rules:

- The tower will be weighed with the container.

- A judge will measure the tower to check that building restrictions have be followed.

- A team member will place the tower in the allowed square footprint.

- Water will be added to the container in units.  After each addition of mass, a judge will determine if the tower has been successful in sustaining the load (this should be pretty obvious).

- The trial is over when either:

a)  the tower has broken

b)  the container is full to capacity

Scoring:

The last mass held successfully by the tower is the "total water mass".

Score = (Total Water Mass) / (Mass of Tower)

example:  	A tower that holds 10.5 L and has a mass of 0.454 grams would have a score

of (10.5)/(0.454) = 23.13